Title
Electromechanical devices MM2EMD
Lecture 4 – Analog electronics
“every idiot can count to one” - Bob Widlar
Dr. Roderick MacKenzie
roderick.mackenzie@nottingham.ac.uk
Summer 2015
@rcimackenzie
Released under

---
Outline of the lecture
No recap of last lecture :)
Finish off digital electronic- Race times
Analog electronics
Operational Amplifiers
What is an op-amp and what are they used for?
Two fundamental op-amp circuits
Inverting amplifier
Particle op-amps
Summing amplifier
Summary

---
Last tip on digital electrons race times
Think about this circuit...
1
1
Let's draw this out in detail
0
0
Slooby from Chicago

---
Last tip on digital electrons race times
If you changed the inputs from 11 to 00 the outputs would not change.
0
1
1
1
Let's draw this out in detail
1
1
0
1
0
0
Slooby from Chicago

---
Last tip on digital electrons race times
The ideal case:
A
A
O
B
1
A
0
1
B
0
1
A
0
1
O
0
time

---
However, you should know that....
All gates have a 'turn on' and 'turn off' time.
This is in effect a time it takes the gate to react to an input - t.
A
A
t
1
A
0
A
0

---
Last tip on digital electrons race times
However every gate takes a finite time to respond (micro seconds).
A
A
O
B
1
A
0
1
B
0
A
0
1
O
0
time

---
Last tip on digital electrons race times
Gates take microseconds to respond.
This means your output can be wrong for up to a microsecond.
The more gates you have the longer theses effects will last for.
Often glitches don't matter, but if you are designing sensitive (fast) circuits, they can be really really important.
A
A
O
B

---
Outline of the lecture
No recap of last lecture :)
Finish off digital electronic- Race times
Analog electronics
Operational Amplifiers
What is an op-amp and what are they used for?
Two fundamental op-amp circuits
Inverting amplifier
Particle op-amps
Summing amplifier
Summary

---
Book chapter
Everything you need for the exam is in this lecture and the example sheet.
However if you would like to read more in depth about this subject:
An Introduction to Mechanical Engineering: Part 1 pages 365 to 371

---
Digital signals
Until now I have only taught you how to use digital electronics to process information.
In digital electronics signals can either be on (1) or off (0) and all information is transmitted and stored using binary numbers.
1
A
However the real world is not binary, think of playing a music on a guitar.....
0

---
Analog signals.
Your guitar produces compression waves in the air that a microphone can pick up.
V
These signals can have any value and are called analog signals.

---
Analog electronics – why?
Why are you going to teach us about analog electronics, is not everything digital nowadays?
TV, music, radio etc.
Yes, but there is always an analog part to any circuit interacting with the real world.
Example....

---
An MP3 recorder as an example of a modern analog and digital system.
V
0.1 mV
Analog to
Digital
converter
Analog
electronics
(amplifier
filters)
mp3
Being able to process analog signals is very important.
And this is what I am going to teach you about in this lecture.
Voltage
Voltage
Voltage

---
Where else will we find analog electronics?
Common applications include:
Audio and video pre-amplifiers
Filters – clean up signals.
Voltage regulators
Analog to digital converters (data acquisition)
Amplifying small signals from sensors before sending the data to a computer
To make all theses circuits you use something called an operation amplifier

---
Outline of the lecture
No recap of last lecture :)
Finish off digital electronic- Race times
Analog electronics
Operational Amplifiers
What is an op-amp and what are they used for?
Two fundamental op-amp circuits
Inverting amplifier
Particle op-amps
Summing amplifier
Summary

---
The operational amplifier
One of the most useful/versatile and widely used analog chips is the operation amplifier.
Op-amp in 8 pin DIP package
Biro

---
“every idiot can count to one”
This is the farther of modern analog electronics - Bob Widlar
He was a genius and eccentric who spent his life designing the very first versions of all the analog chips we are going to learn about in the next couple of lectures.
He said “every idiot can count to one”, meaning that analog electronics hard is harder than digital electronics but often more worth while.

---
The human aspect
“Widlar lived the life of an alcoholic loner, who went on all-night-long bar binges. He liked to fight others when drunk, but regularly overestimated his own abilities in such confrontations. On one occasion he was "absolutely clocked" by the offended Mike Scott, a future CEO of Apple Inc.”
However, the story about Widlar bringing a goat to trim the lawn in front of his office, was incorrect. It was a sheep. He brought her in his Mercedes-Benz convertible for just one day, he later abandoned her in the nearest bar.
Let's look at some of this character designed..

---
What is the purpose of an op-amp
We can guess what they do by the name:
Operational amplifier
An amplifier i.e. something that makes a signal bigger.
And 'operation', think of a mathematical operation.
In effect they are an amplifier that does maths.

---
But what is inside this op-amp?

---
Ahhh...
This is far too complex to understand, so let's just make a model of this complex circuit...
Daniel Braun

---
A model of an op-amp (equivalent circuit)
The Op-amp equivalent circuit has two inputs:
Inverting input (-)
Non-inverting input (+)
-
Vin
Vout
+
And an single output Vout.

---
It contains two resistors
Rin = an input resistance – very high – we can assume this is infinite.
Ro = output resistance – very low – we can assume this is zero (i.e. a short circuit)
Rin
-
Ro
+
So let's further simplify our circuit taking into account the high Rin and the low Ro.

---
That's better
-
Vin
Vout
+

---
A model of an op-amp (equivalent circuit)
The op-amp produces a voltage Vout
A times bigger than Vin
-
A*Vin
Vin
Vout
+
Vin A=Vout
Where A is the gain (or amplification) of the op-amp.

---
'A' tells us how much bigger the output signal will be compared to the input signal.
Vin
Vout
-
Vin
time
Vout
time
+
Vin A=Vout
But what is A for a typical opamp?

---
That depends upon the frequency of input signal...
The gain is non linear, meaning a signal at 10 Hz, will be amplified by 1x105, but signal at 10 kHz will be amplified by only 100.
This will mean your signal will be distorted.
106
105
A – open loop gain
104
103
102
10
107
105
106
103
104
102
10
frequency
Gain (A)
Hartmut Häfele

---
Another problem with this op-amp...
Imagine we had a 0.01V signal at 10 Hz.
What is the gain (A) at 10 Hz?
Vout=VinA
What will Vout be?
106
105
A – open loop gain
104
103
102
10
107
105
106
103
104
102
10
frequency
Gain

---
Another problem with this op-amp...
An output voltage of 10000 Volts?
This seems quite high, especially as op-amps can only run of 5 Volts???
106
105
A – open loop gain
104
103
102
10
107
105
106
103
104
102
10
frequency
Gain

---
Saturating your amplifier (A=1x105)
Ideal case:
A
0.01 V
10000 V
Vin*A=Vout
What will really happen: Your op-amp runs from a 5V supply it will not be able to generate 1000V on the output. The result will be….
A
5 V
0.01 V
Vin*A=Vout
Your signal will be clipped at 5 V.
This seems bad.. how do we fix this??

---
Problems with the op-amp..
Non linear gain
Output clipping
A
5 V
0.01 V
Vin*A=Vout
10
102
103
104
105
106
107
10
102
103
104
106
105
frequency
Gain (A)

---
Outline of the lecture
No recap of last lecture :)
Finish off digital electronic- Race times
Operational Amplifiers
What is an op-amp and what are they used for?
Two fundamental op-amp circuits
Inverting amplifier
Particle op-amps
Summing amplifier
Summary

---
The inverting amplifier
(introducing feedback)
Rf
R1
-
A*V
Vin
Vout
+
0 Volts
To try and solve this problem. We take a proportion of the output and feed it back to the negitave input to reduce the overall gain. Negative feedback loop.

---
The result is a flatter lower gain curve:
This will:
a) Reduce the gain, and help produce a flat gain over a wide range of frequencies.
b) The gain is lower so your device won't saturate.
frequency
Let's analyze this circuit in a bit more detail ....
10
102
103
104
105
106
107
10
102
103
104
106
105
Gain

---
How much gain will this circuit with feedback give us?
To do this we need to write an expression linking the input voltage (Vin) to the output voltage (Vout).
Vin
Vout
time
time
We are going to use Kirchhoff's Current and Voltage Laws to derive this expression.
Vout
Vin

---
Our strategy to derive an equation describing this circuit.
Write an expression relating the input voltages to the voltages at the terminals of the op-amp
Write an expression relating the output of the op-amp to the input terminals of the op-amp
Relate the two expressions
Get the answer
Vout
Vin

---
The inverting amplifier
The inverting amplifier has two external resistors:
Feedback resistor Rf , Input resistor Rin
The input resistance to an op-amp is always very high so we can assume it is infinite so i= 0.
Rf
Looking at the inverting input we can write input
i1=-if
1
A*V
Vout
V
-
+
Vin
Rin
0 Volts
if
i
i1
V+=0V

---
Look at the front end of the circuit
Apply Kirchhoff’s Voltage Law linking the input voltage Vin to the negative input terminal.
size 34 {V_{"in"}=i_{1}R_{1}-V}
Rf
A*V
Vout
V
-
+
Vin
R1
0 Volts
if
i
i1
V+=0V

---
Look at the front end of the circuit
size 34 {V_{"in"}=i_{1}R_{1}-V}
V is an unknown so let's get rid of it with Vout=AV.
Rf
size 34 {V_{"in"}=i_{1}R_{1}-V_{out} over A}
2
But we still don't know i1.
A*V
Vout
V
-
+
Vin
R1
0 Volts
if
i
i1
V+=0V

---
Look at the back end of the circuit
Now, apply Kirchhoff’s Voltage Law linking the output Vout to the negative terminal.
Rf
if
size 38 {V_{out}=i_{f}R_{f}-V}
R1
i
-
A*V
i1
V
Vin
Vout
+
V+=0V

---
Look at the back end of the circuit
size 38 {V_{out}=i_{f}R_{f}-V}
Again V is an unknown so let's get rid of it with Vout=AV.
Rf
size 38 {V_{out}=i_{f}R_{f}-V_{out} over A}
3
But we still don't know if.
A*V
Vout
V
-
+
Vin
R1
0 Volts
if
i
i1
V+=0V

---
Look at the back end of the circuit
Now we have two equations with three unknowns
size 34 {V_{"in"}=i_{1}R_{1}-V_{out} over A}
2
Rf
if
size 38 {V_{out}=i_{f}R_{f}-V_{out} over A}
R1
3
i
-
A*V
i1
V
Vin
But we know that...
Vout
+
V+=0V
i1=-if
1
0 Volts

---
Deriving an expression to relate input and output voltage.
Rf
size 32 {V_{"in"}=i_{1}R_{1}-V_{out} over A}
size 32 {V_{out}=-i_{1}R_{f}-V_{out} over A}
And after some work...
size 30 {V_"in" = {V_"out" [R_1(A+1) +R_f]} over {-R_f A}}
A*V
Vout
V
-
+
Vin
R1
0 Volts
if
i
i1
V+=0V

---
Calculating closed loop gain
Rearrange this expression to get the output over the input or the closed loop gain:
size 32 {V_"out" over V_"in" = {-R_f A} over [ R_r(A+1) +R_f] }
size 32 {G= V_"out" over V_"in" }
Note the negative sine indicates that the output voltage is negative.

---
Closed loop gain:
size 32 {G=V_"out" over V_"in" = {-R_f A} over [ R_r(A+1) +R_f] }
106
105
A – open loop gain
104
103
102
G – closed loop gain
10
107
105
106
103
104
102
10
frequency
Gain

---
At low frequencies we can simplify the equation...
size 32 {V_"out" over V_"in" = {-R_f A} over [ R_r(A+1) +R_f] }
when A>>1, we can write..
You can now build and design any small signal amplifier with any gain by carefully picking the values of Rf and R1.
size 32 {G= V_"out" over V_"in" = - {R_f over R_1}}

---
Example exam question
An inverting amplifier circuit has an input resistance R1=10 k Ohm and a feedback resistance of Rf =1M Ohm.
Using the open circuit gain v.s. frequency plot for the 741 op-amp calculate the exact close loop gain G at 10 Hz.

---
Rearrange the closed loop gain equation
size 30 {G= V_0 over V_i = {-R_f A} over {R_1 (A+1)+R_f} }
size 30 {R_f=1M%OMEGA = 10^{6} %OMEGA }
size 30 {R_1=1k%OMEGA = 10^{4} %OMEGA }
size 30 {G = {-100 A} over {(A+101)} }

---
Example question
Then at 10 Hz, look up the open loop gain A on the graph.
A=1x105
106
105
104
103
Pop A into the equation:
102
size 30 {G = {-100 A} over {(A+101)} }
10
107
105
106
103
104
102
10
Calculate the closed loop gain G:
G=99.899
Gain

---
Your turn
High speed trains must stop when there is an earth quake or the trains will de-rail.
You are designing an earthquake detection system for a new generation of high speed trains.
You are listening for earthquakes with a microphone attached to the side of the tracks.
Earthquakes produce a lot of vibrations at 1000 Hz.
During an earthquake your microphone will produce a 0.1 V sin wave at 1000Hz.
You have designed an amplifier circuit with Rf=1000 Ohm, R1=10 Ohm. What will the output voltage of the amplifier be when an earth quake hits?

---
Your turn
f=1000 Hz
size 30 {R_1=10 %OMEGA}
size 30 {R_f=1k%OMEGA}
size 30 {V_"in"=0.1 V }
106
size 30 { V_"out" over V_i = {-R_f A} over {R_1 (A+1)+R_f} }
105
Rf
104
R1
103
102
10
107
105
106
103
104
102
10
We are looking for the value of Vout.
Gain
Vout
Vin

---
Your turn
size 30 {R_f=1k%OMEGA }
@1000 Hz, A=1x103
106
size 30 {R_1=1k%OMEGA}
105
size 30 { V_0 = {-R_f A V_i} over {R_1 (A+1)+R_f} }
104
103
size 30 { V_"out" = {-1000 x 1x10^{3} 0.1} over {10 (1x10^{3}+1)+1000.0} }
102
10
107
105
106
103
104
102
10
size 30 {V_"out"=-9.082}
Gain

---
Outline of the lecture
Recap of last lecture
What is an op-amp and what are they used for?
Three fundamental op-amp circuits
Inverting amplifier
Practical op-amps
Summing amplifier
Summary

---
Piratical considerations when designing op-amp circuits

---
Using op-amps in the real world.
They all have a small hole in them so you know which way around they go.
Page 1 in the data sheet.

---
Using op-amps in the real world.
NC means not connected
Vcc means a positive supply voltage.
VEE means earth.
You know what IN(-), and IN(+) do, and what output do.
Ignore, the offset pins.

---
Page 2: Information on how to break it.
Or how to avoid breaking it.
Notice the temperate ranges – not that low..

---
Page 3: Gain graphs
106
105
104
103
102
10
107
105
106
103
104
102
10
Gain (A)

---
Outline of the lecture
No recap of last lecture :)
Finish off digital electronic- Race times
Analog electronics
Operational Amplifiers
What is an op-amp and what are they used for?
Two fundamental op-amp circuits
Inverting amplifier
Particle op-amps
Summing amplifier
Summary

---
Mathematics with op-amps
I said at the beginning of the lecture that one major application for op-amps is to do mathematics.
Adding signals together is something you very often have to do in electronics and this is how you do it with an op-amp.

---
The summing amplifier
R3
i3
Rf
if
R2
i2
i
V3
-
R1
i1
V2
V1
Vout
+
0 Volts

---
Mathematics with op-amps
R3
i3
Rf
if
R2
i2
i
V3
-
R1
A*V
i1
V2
V
V1
Vout
+
0 Volts

---
Mathematics with op-amps
R3
Using Kirchhoff’s Voltage Law
size 30 { V_1=i_1 R_1 -V }
size 30 { V_2=i_2 R_2 -V }
size 30 { V_3=i_3 R_3 -V }
size 30 { V_out=i_f R_f -V }
size 30 {V={V_{out} over {A}}}
If Ro = 0
and
As A is very large, v tends to zero and the voltage
 equations may be simplified to:
size 30 { V_3=i_3 R_3}
size 30 { V_1=i_1 R_1}
size 30 { V_{out}=i_f R_f}
size 30 { V_2=i_2 R_2}
V1 = i1R1
V2 = i2R2
Rf
Vout
-
+
0 Volts
if
i
i1
V1
R2
R1
V2
V3
i2
i3
A*V
V

---
Mathematics with op-amps
If the input resistance of the op-amp is high i=0.
Therefore we can write:
R3
size 30 { i_1+i_2+i_3=-i_f }
size 30 { V_1 over R_1 + V_2 over R_2 +V_3 over R_3 = - V_0 over R_f }
size 30 { V_{"out"} = -R_f left [ V_1 over R_1 + V_2 over R_2 +V_3 over R_3 right ] }
Rf
Vout
-
+
0 Volts
if
i
i1
V1
R2
R1
V2
V3
i2
i3
A*V
V

---
Mathematics with op-amps
R3
If
size 30 { R_1=R_2=R_3 }
and
size 30 { R_f=R_1+R_2+R_3 }
size 30 { V_{out}=-[V_1+V_2+V_3]}
i.e. the output voltages are the sum of the input voltages
size 30 { V_{out}=-sum V_{"in"}}
Rf
Vout
-
+
0 Volts
if
i
i1
V1
R2
R1
V2
V3
i2
i3
A*V
V

---
Summary of today's lecture
No recap of last lecture :)
Finish off digital electronic- Race times
Analog electronics
Operational Amplifiers
What is an op-amp and what are they used for?
Two fundamental op-amp circuits
Inverting amplifier
Particle op-amps
Summing amplifier
Summary