Title
Electromechanical devices MM2EMD
Lecture 8 – Analog-to-digital and digitial-to analog converters.
Dr. Roderick MacKenzie
roderick.mackenzie@nottingham.ac.uk
Summer 2015
@rcimackenzie
Released under

---
Outline of the lecture
No recap of last lecture :)
Recap of digital signals
Converting between digital and analog
Digital to analog converters
Analog to digital converters
Flash converters for high speed video
Summary

---
Outline of the lecture
No recap of last lecture :)
Recap of digital signals
Converting between digital and analog
Digital to analog converters
Analog to digital converters
Flash converters for high speed video
Summary

---
Digital signals recap
In lectures 1-3 I taught you about digital electronic.
In digital electronics signals can either be on (1) or off (0) and all information is transmitted and stored using binary numbers.
1
A
In L4 we learnt that the real world is not binary......
0

---
Analog signals recap
Your guitar produces compression waves in the air that a microphone can pick up.
V
These signals can have any value and are called analog signals.

---
Digital v.s. analog signals
A digital signal
1
A
0
An analog signal

---
The MP3 recorder example
Digital circuit to produce MP3s
Analog
electronics
(amplifier
filters)
mp3
An MP3 recorder as an example of a modern analog and digital electronics system.
Voltage
Voltage

---
The MP3 recorder example
Digital circuit to produce MP3s
Analog
electronics
(amplifier
filters)
mp3
You now know all about digital electronics (well quite a lot anyway)
Voltage
Voltage

---
The MP3 recorder example
Digital circuit to produce MP3s
Analog
electronics
(amplifier
filters)
mp3
You now know all about digital electronics
You also know all about analog electronics. (well quite a lot anyway)
Voltage
Voltage

---
The analog/digital divide
Digital circuit to produce MP3s
Analog
electronics
(amplifier
filters)
mp3
But what you don't know yet is how to convert analog signals in to binary or digital codes.
Voltage
Voltage

---
Converting analog signals into binary signals.
Digital circuit to produce MP3s
Analog
electronics
(amplifier
filters)
mp3
?
Voltage
Voltage
Voltage
Voltage

---
Analog to digital converter
Every time you want a computer to interact with the real word you will need a analog to digital converter.
Voltage
Voltage
André Karwath
Xell

---
Outline of the lecture
No recap of last lecture :)
Recap of digital signals
Converting between digital and analog signals
Digital to analog converters
Analog to digital converters
Flash converters for high speed video
Summary

---
Digital to analog converter
Voltage
Voltage
ZookPS3

---
Digital to analog converter
Before we look at something complex like music, let's look at just converting on number.
 0.5 V
10000
 0.25 V
01000
And this is the circuit we use to do this convert one binary number to a analog number....

---
The R2R ladder
This is THE circuit used to convert all digital signals to analog signals.
Vout
R
2R
It is also very elegant

---
The R2R ladder
This is the analog output of the circuit.

---
The R2R ladder
These are the digital inputs to the circuit.

---
The R2R ladder
1V
We can apply either 1 V or 0 V to the inputs.
This would represent 00000

---
Let's look at pin 1
Let's apply 1V to the first input and see what output we get at Vout.
This would represent the binary number 10000
To do this we need to analyze the circuit.

---
Analyze the last two resistors
They are in parallel so...
size 32 {{1 over R_"new" } = 1 over {2R} + 1 over {2R}}
size 32 { R_"new" = R}

---
We can represent them using one resistor with value R

---
Now look at these two resistors on the end.
We can turn them into one resistor with value 2R

---
Giving...

---
Another two parallel resistors...
size 32 {{1 over R_"new" } = 1 over {2R} + 1 over {2R}}
Now let's turn these two parallel resistors into one resistor.
size 32 { R_"new" = R}

---
Gives...
Which can be converted into one resistor....

---
Two resistors in series..
Which can be converted into one resistor....

---
What voltage will we get if we put

---
Another two resistors in parallel
size 32 {{1 over R_"new" } = 1 over {2R} + 1 over {2R}}
Which again gives one resistor with a value of R.
size 32 { R_"new" = R}

---
Leaving us with.....
What can we do now??

---
Leaving us with.....
Join these two resistors together.

---
And we now have...
This looks complicated so let's just move things around to make them less scary.

---
Move Vout to the top – why not?
Looking a bit like a potential divider now.
Let' get rid of the grounds.

---
A more simple circuit
Now let's rearrange this circuit to make it look like something we may understand.

---
What does this remind you of?

---
It's a potential divider
size 32 {V_"out"=1V*{ {2R} over {2R+2R} }}
Therefore, Vout =0.5 V

---
If the first resistor is switched on we get Vout=0.5 on the output.
Vout=0.5
<-Remember this at least for the next 15 min

---
Now lets look at the second digital input.
Let's find out what Vout will be when we turn this on.
This would represent the binary number 01000

---
Let's look at input 2 (This is the last pin we will examine)

---
Starting from the right hand side again.
Two resistors in parallel
size 32 {{1 over R_"new" } = 1 over {2R} + 1 over {2R}}
size 32 { R_"new" = R}

---
Gives....

---
R + in series gives..

---
Gives 2R

---
2R and 2R in parallel gives
size 32 {{1 over R_"new" } = 1 over {2R} + 1 over {2R}}
size 32 { R_"new" = R}

---
This gives R
Tidying up R+R..

---
We are left with this circuit
Let's get rid of the ground signs because they are confusing.

---
That's better
For the moment let's also get rid of Vout.

---
This is looking more simple
Join R and 2R together.

---
Even more manageable
3R
Let's redraw this in a more easy to understand form..

---
Two resistors in parallel.
3R
size 32 {{1 over R_"new" } = 1 over {3R} + 1 over {2R}}
size 32 { R_"new" = 1.2R}

---
Now we just have a potential divider
What's this circuit?
1.2R

---
Now we just have a potential divider
The voltage across 1.2 R is.
size 32 { V_1}
1.2R
size 32 {V_1=1V {{1.2R} over {2R+1.2R}}}
size 32 { 0.375 V}

---
Superimposing this voltage on our original circuit.
1.2R
0.375 V
0.375 V
0.375 V

---
Another potential divider
0.375 V
size 36 {V_"out"=0.375{{2R} over { R+2R }}=0.25V}

---
If the second resistor is switched on we get Vout=0.25 on the output.
Vout=0.25

---
Life is short – so we won't look at any more pins
I will just tell you what happens for the rest of the pins now.

---
Input 1 representing binary 10000
Vout=0.5

---
Input 2 representing binary 01000
Vout=0.25

---
Input 3 representing binary 00100
Vout=0.125 V

---
Input 4 representing binary 00010
Vout=0.0625 V

---
Input 5 representing binary 00001
Vout=0.03125 V

---
Inputs 1, 2, 3, 4, and 5 - (11111)
Vout=0.5 V+0.25 V +0.125 V + 0.0625 V + 0.03125 V
Vout=1 V

---
We can turn on any combination on i.e. 11000
Vout=0.5 V+0.25 V
Vout=0.75 V

---
Question
Does this remind you of anything?

---
Answer
Sort of counting in binary...

---
If we connect the R2R ladder to the binary output from a chip...
We can generate any voltage between 0 V and 1 V
2
2
1/0
1/0
1/0
0V
Digital circuit/chip
0V
Binary number
0
8
4

---
R2R ladder resolution
size 32 {resolution="Maximum output voltage" over "number of combinations"}
2
2
1/0
1/0
1/0
0V
Digital circuit/chip
0V
Binary number
0
8
4

---
The more pins we have
The finer the resolution we get.
size 32 {resolution="Maximum output voltage" over "number of combinations"}
2
2
2
0V
1/0
1/0
1/0
1/0
1/0
1/0
1/0
1/0
1/0
0
512
Binary number
Digital circuit/chip

---
We can now make any shape analog signal we want.
Time
2
2
Voltage
Nmnogueira

---
If we attach a speaker we get a tone.
Time
Voltage

---
Outline of the lecture
No recap of last lecture :)
Recap of digital signals
Converting between digital and analog
Digital to analog converters
Analog to digital converters
Flash converters for high speed video
Summary

---
Analog to digital converter
Voltage
Voltage

---
Comparators basics
Before we can learn about A2D converters we need to learn about comparators.
+
-
Comparators look just like an op-amp, in fact you can use an op-amp as a low performance comparitor, but you are better off getting a specially designed chip like the LM393.
Stuuf

---
Comparators basics
Comparators compare two voltages:
V+
V-
For example...

---
Compactors basics
If V+ is BIGGER than V- it will output a 1 V
If V+ is SMALLER than V- it will output a 0 V
V+
+
1 V or 0V
V-
-
For example...

---
Comparators
If V-=4 V and V+=2 V it will output 0 V.
+
2 V
0 V
-
4 V
For example...

---
Comparators
If V-=4 V and V+= 5 V it will output V 1.
+
5 V
1 V
-
4 V
We now know everything we need to implement an analog to digital converter.

---
Stick our comparator on the output of and R2R ladder
This is the clever part.
Imagine we want to find out what voltage Vmeasure is.
Vmeasure
+
0
-
2
2
Vmeasure
0
0
0
0
0

---
Binary 1
We start increasing the voltage given by the R2R ladder.
Vmeasure
0.03125 V
+
0
-
2
2
Vmeasure
0
0
0
0
1

---
Binary 2
Vmeasure
0.0625 V
+
0
-
2
2
Vmeasure
0
0
0
1
0

---
Binary 3
Vmeasure
0.093750 V
+
0
-
2
2
Vmeasure
0
0
0
1
1

---
Binary 4
Vmeasure
0.125 V
+
0
-
2
2
Vmeasure
0
0
1
0
0

---
Binary 5
Vmeasure
0.15625 V
+
0
-
2
2
Vmeasure
0
0
1
0
1

---
Binary 6 – and the output bit flips
0.18750 V
Vmeasure
+
1
-
2
2
Vmeasure
0
0
1
1
0

---
Binary 6 – and the output bit flips
The output from the compactor has now flipped.
So we know that the voltage must be close to 0.01875 V.
0.18750 V
Vmeasure
+
1
-
2
2
Vmeasure
0
0
1
1
0

---
Outline of the lecture
No recap of last lecture :)
Recap of digital signals
Converting between digital and analog
Digital to analog converters
Analog to digital converters
Flash converters for high speed video
Summary

---
Disadvantages of R2R based converters
The problem with the analog to digital converter based on the R2R ladder is that is takes a finite amount of time to count up.
This means conversion is slow.
However they are low cost and you do find them in lots of places – such as in volt meters.
The flash converter for video and other speed applications.
André Karwath

---
Video data
Pixel
3000 elements (x)
To capture video we will need to convert all these pixels (voltages) to binary numbers instantly.
There is no time for counting and using R2R ladders.
3000 elements (y)

---
The Flash converter
Think about these resistors
1 V
What will the voltage here?

---
The Flash converter
Think about these resistors
1 V
0.25 V

---
The Flash converter
Think about these resistors
1 V
0.5 V
0.25 V

---
The Flash converter
Think about these resistors
1 V
0.75 V
0.5 V
0.25 V

---
The Flash converter
Vin
1 V
0.75 V
0.5 V
0.25 V
Connect some comparitors

---
The Flash converter
Vin
1 V
0.75 V
+
-
+
0.5 V
-
0.25 V
+
-

---
The Flash converter
0 V
If we have 0 V input we will get all 0's out.
1 V
0.75 V
+
0
-
+
0.5 V
0
-
0.25 V
+
0
-

---
The Flash converter
0.26 V
If we have 0.26 V input we will get 001 out.
1 V
0.75 V
+
0
-
+
0.5 V
0
-
0.25 V
+
1
-

---
The Flash converter
0.51 V
If we have 0.51 V input we will get 011 out.
1 V
0.75 V
+
0
-
+
0.5 V
1
-
0.25 V
+
1
-

---
The Flash converter
0.9 V
If we have 0.9 V input we will get 111 out.
1 V
0.75 V
+
1
-
+
0.5 V
1
-
0.25 V
+
1
-

---
The Flash converter
0.9 V
Notice the output is not binary code.
We will therefore need a digital circuit to convert it to binary.
1 V
0.75 V
+
1
-
+
0.5 V
1
-
0.25 V
+
1
-

---
The Flash converter
0.9 V
1 V
0.75 V
+
-
Binary encoder circuits.
+
0.5 V
-
0.25 V
+
-

---
Outline of the lecture
No recap of last lecture :)
Recap of digital signals
Converting between digital and analog
Digital to analog converters
Analog to digital converters
Flash converters for high speed video
Summary